## Slide 1: Network Layer: IPv4 Static Routing
Lecture 11 | CSE421 – Computer Networks
Department of Computer Science and Engineering School of Data & Science

## Slide 2: Objectives
Static Routing
Standard static routing
  Directly Attached / Connected
  Next Hop / Recursive
Default Routing
Floating Static Routing

## Slide 3: Learning About Networks
A router can learn about remote networks in one of two ways:
Manually - Remote networks are manually entered into the route table using static routes.
Dynamically - Remote networks are automatically learned using a dynamic routing protocol.
Notes: 3
6.1.1.1

## Slide 4: Learning About Networks
20.20.20.0/30
Network | Exit Int
192.168.10.0/24 | G0/0
192.168.11.0/24 | G0/1
209.165.200.224/30 | S0/0/0
Network | Exit Int
10.1.1.0/24 | G0/0
10.1.2.0/24 | G0/1
209.165.200.224/30 | S0/0/0
220.20.20.0/30 | G0/2
Directly connected
Directly connected
S0/0/0
S0/0/1
Table of R1
Table of R2
10.1.1.0/24
S0/0/0
10.1.2.0/24
S0/0/0
192.168.10.0/24
S0/0/0
192.168.11.0/24
S0/0/0

## Slide 5: Static Route
Manually configured route
Used to reach networks not directly connected
Does not update automatically
Changes must be applied manually
Notes: If there is no dynamic routing protocols

## Slide 6
Static Routes are often used to:
Reach a specific remote network
Set a default route (gateway of last resort)
Provide a backup path (floating static route)
Reduce routing table entries (summarization)
Static Route Types
Notes: 6
Reduce the number of routes advertised by summarizing several contiguous networks as one static route

## Slide 7: Static Route : How??
R1(config)#
20.20.20.0/30
ip route
Parameter 1
Parameter 2
Exit interface or next hop IP address
The remote network address
command
Subnet Mask
Parameter 3
10.1.1.0
ip route
255.255.255.0
S0/0/0
209.165.200.226
R1(config)#
Notes: 7
6.2.1.1

## Slide 8: Routing Table of R1 after the static route command
R1# show ip route
C 192.168.10.0/24 is directly connected, GigabitEthernet0/0
C 192.168.11.0/24 is directly connected, GigabitEthernet0/1
C 209.165.200.224/30 is directly connected, Serial0/0/0
S 10.1.1.0/24 is directly connected, Serial0/0/0
R1# show ip route
C 192.168.10.0/24 is directly connected, GigabitEthernet0/0
C 192.168.11.0/24 is directly connected, GigabitEthernet0/1
C 209.165.200.224/30 is directly connected, Serial0/0/0
S 10.1.1.0/24 [1/0] via 209.165.200.226
Using Exit interface
Using next hop IP address

## Slide 9: Recursive Lookup
R1# show ip route
C 192.168.10.0/24 is directly connected, GigabitEthernet0/0
C 192.168.11.0/24 is directly connected, GigabitEthernet0/1
C 209.165.200.224/30 is directly connected, Serial0/0/0
S 10.1.1.0/24 [1/0] via 209.165.200.226
20.20.20.0/30
Router R1 receives a packet which has the destination address is 10.1.1.24
How many times did the Router R1 look up the routing table?

## Slide 10: Routing Table of R1 after the static route command
R1# show ip route
C 192.168.10.0/24 is directly connected, GigabitEthernet0/0
C 192.168.11.0/24 is directly connected, GigabitEthernet0/1
C 209.165.200.224/30 is directly connected, Serial0/0/0
S 10.1.1.0/24 [1/0] via 209.165.200.226
Using next hop IP address
Type of route:
S - Static
Destination Network
Next Hop IP
Or, Exit Interface
Administrative
Distance
Cost of Path
AD : The trustworthiness of the source of the route

## Slide 11: Default Route
All PCs of R1 and R2 need to go to the Internet ….
ip route 0.0.0.0 0.0.0.0 s0/0/1

## Slide 12: ip route Command
ip route
Exit interface or next hop IP address
The remote network address
Subnet Mask
0.0.0.0
ip route
0.0.0.0
S0/0/1
R2(config)#
Any network
What about R1?
ip route 0.0.0.0 0.0.0.0 s0/0/0
Notes: 12
6.2.1.1

## Slide 13: Default Static Route in the Routing Table
R1# show ip route
C 192.168.10.0/24 is directly connected, GigabitEthernet0/0
C 192.168.11.0/24 is directly connected, GigabitEthernet0/1
C 209.165.200.224/30 is directly connected, Serial0/0/0
S 10.1.1.0/24 [1/0] via 209.165.200.226
S* 0.0.0.0/0 is directly connected, Serial0/0/0

## Slide 14: Floating Static Routing
Source : https://study-ccna.com/floating-static-route/

## Slide 15: Floating Default Static Routing
R1(config)#ip route 0.0.0.0 0.0.0.0 S0/0/0
S* 0.0.0.0/0 is directly connected, S0/0/0
S* 0.0.0.0/0 is directly connected, S0/0/1
Both has same cost same AD. Which one to use?
5
AD > default Value
R1(config)#ip route 0.0.0.0 0.0.0.0 S0/0/1
R1 Routing Table (Partial)
Present in Routing Table
Present in Router Configuration File

## Slide 16: Static Route Advantages
Simple and predictable
More secure (not advertised)
Low CPU/memory usage
Notes: 16
Advantage of static routing
It is most secure way of routing, since no information is shared with other routers.
It puts no overhead on resources such as CPU or memory.
No routing algorithm or update mechanisms are required. Therefore, extra resources (CPU and memory) are not required.
It is easy to implement.

## Slide 17
Time-consuming to configure
Not scalable for large networks
No automatic failover
Requires full network knowledge
Static Route Disadvantages
Notes: 17
6.1.1.2

## Slide 18: The End